## Slide 1: Design for mid-block traffic signals adjacent rail

## Slide 2: KiwiRail design guide
Soon to be published
Key design principles:
  Minimise the need for at-grade crossings
  Seek awareness by users
  Seek compliance by users
  Provide safe accessible and practical use
  Provide appropriate and consistent treatments
  Treatments should be maintainable

## Slide 3: KiwiRail design guide – traffic signal integration
Section 5.4.3: Path Signals for Parallel Pathways
Integration required when a pathway crosses a road within 30m of a level crossing
Four interfaces are available:
  Pre-warning (train approaching, terminate phase)
  Pre-emption (cut the traffic signal green for redundancy)
  Pre-cancellation (terminate the ped/cycle phase)
  Hold down (traffic signals can keep barriers down until ped/cycle phase has completed clearance)

## Slide 4
Layout considerations:
Pole locations – both approaches (careful positioning of far side poles…)
Conflicting displays
Rail displays facing down paths
Yellow hatching?
Red arrows for turning cyclists

## Slide 5: Traffic Signal Considerations
Traffic lights must be in red prior to barriers start
  Take into account travel time so people aren’t ‘trapped’ at railway
Allow the pedestrian/cycle crossing to run safely during train phase
  Delay the start to ensure barriers are down
  Reintroduction / walk for green (reintroduction reduces unnecessary delay below)
  Use pre-cancellation to know when train is almost clear to stop ped running
  Hold barriers down until clearance complete for those drivers who go when barriers start rising
Sequence the end of the train phase
  Use the ‘Barriers rising’ circuit to run the intergreen prior to barriers vertical
Other considerations
  Use a max timer (e.g. 5mins) on the train phase due to pre-warning only and no train
  Earthing must be separated and 230V traffic circuits isolated from railway interface (no direct circuits)
  Consider all scenarios of when train phase called in cycle

## Slide 6: Traffic Signal Considerations

## Slide 7: Advice & feedback
Engage KiwiRail early – lots of people will be involved
Talk to someone who’s been through it before
Have good documentation
Feedback sought from KiwiRail:
Is there value in traffic and rail signal experts working together?
Feedback on the design guide so it can be improved
Where would their guidance documentation be housed for that relating to traffic signal engineers?

## Slide 8: The end… questions?
John.Kinghorn@hcc.govrt.nz
Thomas.Wood@kiwirail.co.nz