## Slide 1: Tron Topics

## Slide 2: Hamilton Operations

## Slide 3: Growth

## Slide 4: The Case for Advanced Network Management
Focus is on moving from reactive to proactive, by focusing on:
  The collection of good data to inform decisions
  Real-time monitoring and management of events
  Optimisation of the network
  Better informed customers
Economically easy to justify

## Slide 5: Current Situation
Business Case with NZ Transport Agency
Partnered with CitySafe team for operations room
Working on implementing the obvious stuff like
  Better data
  Systems
  Resourcing
  Resilience
  Optimisation

## Slide 6: Things We Do Differently (because we’re special)

## Slide 7: Pedestrian Priority
At mid-block crossings, we give pedestrians an immediate cross phase (50k zones or less)
  Approach gap set to zero
  Minimum road phase set to say 25s
Why?
  If we replace a zebra with signals, pedestrians end up with a worse LoS if they now have to wait for a gap (and road phase usually runs to max)
  Why look for a gap when our intersections don’t in Mlink anyway?
  Confirmation, ped approach and signals change
  No need for walk cancellation
  It’s the only way to ensure your staggered SIMPED crossings run properly!!
  Increased compliance from vehicles and pedestrians

## Slide 8: SCATS Communication
We run all our sites network (i.e. we don’t use Eltima)
A local ISP built us a private Layer 2 network
  “Star of stars” design
  Fibre backhaul (~1/3rd are fibre sites)
  Point to point wifi links between close sites
  75% cheaper than our previous copper network!
  (and it supports CCTV cameras)
A managed router is located in each traffic signal cabinet
  Polls the controller for it’s site number
  Converts analogue comms to digital
  Establishes the network link to SCATS

## Slide 9: Current Initiatives

## Slide 10: CCTV analytics
Incident alert (broken down vehicles)
  Works in principle, but too much bandwidth and it’s not quite there
Pedestrian and vehicle classification/counting
  Works well, scan image every 30s, low bandwidth
  Intend to use for alerting of groups of pedestrians
Now testing edge devices

## Slide 11: Addinsight (travel time)
Easy way to get good visibility of network operation
  Learns what is ‘normal’ and only alerts you to abnormal
  Offers historical insights for optimization
  Shows effects of road closures & traffic management
  Cheap & fast deployment (leased solution)

## Slide 12: Transport Dashboard MVP
Situational awareness via “single pane of glass”
  Combines Addinsight, google, customer complaints, bus locations, and SCATS (alarms and unusual volumes, based on scenarios – incl pulsing)
  Removes the need to monitor multiple windows
  Smarter by combining multiple data sources (e.g. text alerts)
  Machine learning to get better at sending the right alerts

## Slide 13: Questions?

## Slide 14: Name Change?
Why should we change our name?
To better reflect what we do
  Develop standards (P43)
  Advise and submit on rules e.g. TCD
  Much more than just a user group
To align better with Engineering NZ (recent name change)
Australia has recently done the same with SMUG
Because it means nothing to those who don’t know the acronym (and always gets some ribbing)
Suggested name: Traffic Signals NZ
VOTE on Slido:
No – keep it SNUG
Yes but different name
Yes – Traffic Signals NZ